###### TEST CASES FOR MPLS - RSP
##### Created on – 07/06/2017

# 1. INTRODUCTION
This document lists test cases identified to run MPLS for RSP router project . Document is structured to provide , with each test case the set up required and output expected when each is executed.
Test cases (in section 3) are designed for a single DUT , how DUT is programmed and how it behaves in different network scenarios followed by complete topology test cases which involve upto three DUTs.
# 2. TEST SETUP FOR SINGLE DUT
Mentioned test setup will provide a functional DUT ready to take low level MIB commands . Two interafces of DUT are connected to STC ports . STC ports are functional and can receive and trasmit packets .

      DUT
      STC-1
       STC-2

Eth0
10.0.1.55
Eth1
20.0.2.55
9/3 10.0.1.32
9/4 20.0.2.32

Configuration needed for this setup :
AT DUT
Run script install_tile.sh to set suitable run environemet .
Cd /rsp/metacli
sh install_tile.sh /
Now run start_setup script to start nbase-stub . Router-dcl and confd
start_setup
Now enter CLI mode
cli
System is now ready to take MIB based commands
To start fast path on DUT :
fast-path.sh start
linux-fp-sync.sh start
Now configure interafce eth0 and eth1
ifconfig eth0 10.0.1.55
ifconfig eth1 20.0.2.55

# 3. TEST CASES
Test cases listed are run over a single DUT . DUT will play different role in each test case . It will simulate ingress , transit or egress router.
## 3.1 Create Product Entities
This test case creates all entities needed to run MPLS static LSP feature.
All other test cases will use this case as base configuration followed by their own .
Test Input :
config
unhide hidemib-group
newscope
DC-I3-MIB i3EmuTable i3EmuEntry 1 i3EmuAdminStatus adminStatusUp
commit
top
DC-LMGR-MIB dcLmgrLsrEntityTable dcLmgrLsrEntityEntry 1
dcLmgrLsrEntityTranAddrType ipv4
dcLmgrLsrEntityTranAddrLen 4
dcLmgrLsrEntityTranAddr 41:03:03:03
dcLmgrLsrAutoStaticLsps true
dcLmgrLsrDisplayPhpXCs true
dcLmgrLsrEntityAdminStatus adminStatusup
commit
top
DC-I3-MIB i3EiTable i3EiEntry 1 1 0 15 i3EiIfFlags broadcast,multicast
top
DC-I3-MIB i3EaTable i3EaEntry 1 1 0 15 ipv4 0a:00:01:37
i3EaPrefixLen 32
i3EaAddressAdvertise true
i3EaBcastDestAddr ff:ff:ff:ff
commit
top
DC-I3-MIB i3EiTable i3EiEntry 1 1 0 16 i3EiIfFlags broadcast,multicast
top
DC-I3-MIB i3EaTable i3EaEntry 1 1 0 16 ipv4 14:00:02:37
i3EaPrefixLen 32
i3EaAddressAdvertise true
i3EaBcastDestAddr ff:ff:ff:ff
commit
top
DC-I3-MIB i3EmTable i3EmEntry 1 1 0
i3EmLabelSpace gen
i3EmGlobalLabelSpace true
i3EmAdminStatus adminStatusUp
commit
top
DC-I3-MIB i3EmTable i3EmEntry 1 1 15
i3EmAdminStatus adminStatusUp i3EmIfDataOnly true i3EmLabelSpace gen i3EmSignallingCaps dataOnlyIf i3EmGlobalLabelSpace true
i3EmLdpEgressLabelUsage php
commit
top
DC-I3-MIB i3EmTable i3EmEntry 1 1 16
i3EmAdminStatus adminStatusUp i3EmIfDataOnly true i3EmLabelSpace gen i3EmSignallingCaps dataOnlyIf i3EmGlobalLabelSpace true i3EmLdpEgressLabelUsage php
commit
top
DC-RLDF-MIB dcLmgrLdfEntityTable dcLmgrLdfEntityEntry 1
dcLmgrLdfEntityI3EntIndex 1
dcLmgrLdfEntityGALSupport true
dcLmgrLdfEntityEnableIPI true
dcLmgrLdfEntityAdminStatus adminStatusUp
commit
top
Expected Output
Following config should be verified after this test case is run
1. do show DC-I3-MIB i3EmuTable
I3
EMU I3 EMU OPER
INDEX STATUS
---------------------
1 operStatusUp
2. do show DC-LMGR-MIB dcLmgrLsrEntityTable dcLmgrLsrEntityEntry
DC
LMGR
LSR DC DC
ENTITY DC LMGR LSR LMGR LMGR DC LMGR
LSR ENTITY OPER LSC LDB LSR STATIC
INDEX STATUS STATUS COUNT P2MPACTIVE
-------------------------------------------------
1 operStatusUp active 0 false
3.do show DC-RLDF-MIB dcLmgrLdfEntityTable dcLmgrLdfEntityEntry
DC
LMGR
LDF
ENTITY DC LMGR LDF
LSR ENTITY OPER
INDEX STATUS
----------------------
1 operStatusUp
4. ngctl list
Look for these nodes :
mpls_global_ilm, split_eth1, mux_eth1, split_eth0 , mux_eth0
These should be created in response to above configuration.
>>>>>>>>>>
 For rest of the test cases we will assume Test case 3.1 configuration is running
 All test cases that follow are build over test case 3.1
<<<<<<<<<<
## 3.2 Create Static transit LSP
This test case will program DUT as transit router . DUT is configures to receive MPLS packet with top label 20 and transmit with label swapped to 30 .
Packet flow can be tested for this configuration by generating a MPLS labeled packet from STC port 9/3 . A mpls packet with label 30 will be received at STC port 9/4 .
Test Input- 1 :
Configuration in test 3.1 followed by:
MPLS-LSR-STD-MIB mplsOutSegmentTable mplsOutSegmentEntry 1 1
mplsOutSegmentInterface 16
mplsOutSegmentPushTopLabel true mplsOutSegmentTopLabel 30
mplsOutSegmentNextHopAddrType ipv4 mplsOutSegmentNextHopAddr 14:00:02:20
commit
top
MPLS-LSR-STD-MIB mplsInSegmentTable mplsInSegmentEntry 1 1 mplsInSegmentInterface 15 mplsInSegmentLabel 20
commit
top
MPLS-LSR-STD-MIB mplsXCTable mplsXCEntry 1 1 1 1 mplsXCAutoStaticXC yes mplsXCAdminStatus up mplsXCLspId 00:00:00:01
commit
top
Expected output
1. do show MPLS-LSR-STD-MIB mplsXCTable mplsXCEntry
DC
LMGR MPLS MPLS
LSR MPLS MPLS XCIN XCOUT
ENTITY XCIN XCOUT MPLS SEGMENT SEGMENT
LSR MPLS SEGMENT SEGMENT MPLS XCOPER IF IF
INDEX XCINDEX INDEX INDEX XCOWNER STATUS INDEX INDEX
----------------------------------------------------------------------
1 1 1 1 snmp up 15 16
2. do show MPLS-LSR-STD-MIB mplsOutSegmentTable mplsOutSegmentEntry
DC MPLS
LMGR OUT
LSR MPLS SEGMENT MPLS MPLS
ENTITY OUT TOP OUT OUT
LSR SEGMENT LABEL SEGMENT SEGMENT
INDEX INDEX PTR XCINDEX OWNER
--------------------------------------------
1 1 1 snmp

3.do show MPLS-LSR-STD-MIB mplsInSegmentTable mplsInSegmentEntry
DC
LMGR
LSR MPLS IN
ENTITY MPLS IN SEGMENT MPLS IN MPLS IN
LSR SEGMENT LABEL SEGMENT SEGMENT
INDEX INDEX PTR XCINDEX OWNER
--------------------------------------------
1 1 1 snmp

4. ngctl list
Look for newly created nodes
mplsnhlfe_XX , mplsether_XX
mpls_global_ilm, split_eth1, mux_eth1, split_eth0 , mux_eth0 nodes will also exist created on running test case 3.1 .
Test Input – 2
Using Spirent , send MPLS packet with label 20 from port 9/3 .
Expected Output
MPLS packet with label 30 should be received at Spirent port 9/4
(Traffic is received at DUT on interface eth0 , packet label is swapped and sent out via interface eth1)
## 3.3 Delete Static Transit LSP
This test case is written to test deletion of a Transit LSP . Deletion is user intended and caused by direct MIB configuration .
Test input
Test case 3.1 and 3.2 followed by following configuration:
no MPLS-LSR-STD-MIB mplsXCTable mplsXCEntry 1 1 1 1
commit
no MPLS-LSR-STD-MIB mplsOutSegmentTable mplsOutSegmentEntry 1 1
commit
no MPLS-LSR-STD-MIB mplsInSegmentTable mplsInSegmentEntry 1 1
commit
Expected Output
1. do show MPLS-LSR-STD-MIB mplsXCTable mplsXCEntry
% No entries found.
2.do show MPLS-LSR-STD-MIB mplsInSegmentTable mplsInSegmentEntry
% No entries found.
3. do show MPLS-LSR-STD-MIB mplsOutSegmentTable mplsOutSegmentEntry
% No entries found.
4. ngctl list
There should NOT exist these nodes :
mpls_global_ilm, split_eth1, mux_eth1, split_eth0 , mux_eth0
mplsnhlfe_XX , mplsether_XX .
Test Input – 2
Using Spirent , send MPLS packet with label 20 from port 9/3 .
Expected Output
No MPLS packet should be received at Spirent port 9/4
(Traffic is received at DUT on interface eth0 , no programming is found corresponding to label 20 and thus packet is dropped)
## 3.4 Create Static Egress LSP
This test case will program DUT as egress router . Labeled packets will terminate here and forwarded further as IP packets.
Packet flow can be tested by sending labeled packet from STC-2(port 9/4) . Packet will land on eth1 of DUT , label will be looked up and popped and IP packet will be forwarded out based on destination IP of packet . DIP is set to 10.0.1.32 , So packet will land on STC1(port 9/3)
Test Input:
Test case 3.1 followed by:
MPLS-LSR-STD-MIB mplsInSegmentTable mplsInSegmentEntry 1 2 mplsInSegmentInterface 16 mplsInSegmentLabel 30
commit
top
MPLS-LSR-STD-MIB mplsXCTable mplsXCEntry 1 2 2 0 mplsXCAutoStaticXC yes mplsXCAdminStatus up mplsXCLspId 00:00:00:02
commit
top
Expected Output
1. do show MPLS-LSR-STD-MIB mplsInSegmentTable mplsInSegmentEntry
DC
LMGR
LSR MPLS IN
ENTITY MPLS IN SEGMENT MPLS IN MPLS IN
LSR SEGMENT LABEL SEGMENT SEGMENT
INDEX INDEX PTR XCINDEX OWNER
--------------------------------------------
1 2 2 snmp
2. do show MPLS-LSR-STD-MIB mplsXCTable mplsXCEntry
DC
LMGR MPLS MPLS
LSR MPLS MPLS XCIN XCOUT
ENTITY XCIN XCOUT MPLS SEGMENT SEGMENT
LSR MPLS SEGMENT SEGMENT MPLS XCOPER IF IF
INDEX XCINDEX INDEX INDEX XCOWNER STATUS INDEX INDEX
----------------------------------------------------------------------
1 2 2 0 snmp up 16 0
3. ngctl list
Check for these newly created vnb nodes :
mpls_vrf0 , split_mpls_vrf0, mux_mpls_vrf0, mux_mpls_ilm_global, mplsnhlfe_XX, mux_eth1, split_eth1, mpls_ilm_global
Test Input – 2
Using Spirent , send MPLS packet with label 30 from port 9/4 .
Expected Output
IP packet with should be received at Spirent port 9/4
(Traffic is received at DUT on interface eth1 , packet label is popped and packet is sent out based on destination IP address . Packet DIP is 10.0.1.32 and therefore packet is sent out via eth0)
## 3.5 Delete Static Egress LSP
This test case is written to test deletion of a Egress LSP . Deletion is user intended and caused by direct MIB configuration.
Test Input
Test case 3.1 and 3.4 followed by:
MPLS-LSR-STD-MIB mplsXCTable mplsXCEntry 1 2 2 0
commit
top
MPLS-LSR-STD-MIB mplsInSegmentTable mplsInSegmentEntry 1 2
commit
top
Expected Output
1. do show MPLS-LSR-STD-MIB mplsXCTable mplsXCEntry
% No entries found.
2. ngctl list
There should NOT exist these nodes :
mpls_vrf0 , split_mpls_vrf0, mux_mpls_vrf0, mux_mpls_ilm_global, mplsnhlfe_XX, mux_eth1, split_eth1, mpls_ilm_global
Test Input – 2
Using Spirent , send MPLS packet with label 30 from port 9/4 .
Expected Output
No packet should be received at Spirent port 9/4
(Traffic is received at DUT on interface eth1 , No configuration is found for label 30 and thus packet is dropped)
## 3.6 Create Static Ingress LSP
This test case will program DUT as ingress router . IP packets enter MPLS network via this router . Label(s) are pushed onto IP packet and injected into MPLS network .
Packet flow can be tested by sending IP packet from STC-2(port 9/3) . Packet will land on eth0 of DUT , DIP based lookup will happen , configured labels will be pushed and packet will be forwarded out via configured interface (eth1) to land on STC-2 (port 9/4)
Test Input
Test case 3.1 followed by
MPLS-LSR-STD-MIB mplsOutSegmentTable mplsOutSegmentEntry 1 2
mplsOutSegmentInterface 16
mplsOutSegmentPushTopLabel true mplsOutSegmentTopLabel 40
mplsOutSegmentNextHopAddrType ipv4 mplsOutSegmentNextHopAddr 14:00:02:20
commit
top
MPLS-LSR-STD-MIB mplsXCTable mplsXCEntry 1 3 0 2 mplsXCAutoStaticXC yes mplsXCAdminStatus up mplsXCLspId 00:00:00:03
commit
top
DC-RLDF-MIB dcLmgrLdfFtnStaticTable dcLmgrLdfFtnStaticEntry 1 1 ipv4 28:00:04:20 32 dcLmgrLdfFtnStatOutLbl 40 dcLmgrLdfFtnStatOutIfIdx 16
commit
top

Expected Output
1. do show MPLS-LSR-STD-MIB mplsXCTable mplsXCEntry
DC
LMGR MPLS MPLS
LSR MPLS MPLS XCIN XCOUT
ENTITY XCIN XCOUT MPLS SEGMENT SEGMENT
LSR MPLS SEGMENT SEGMENT MPLS XCOPER IF IF
INDEX XCINDEX INDEX INDEX XCOWNER STATUS INDEX INDEX
----------------------------------------------------------------------
1 3 0 2 snmp up 0 16
2.do show MPLS-LSR-STD-MIB mplsOutSegmentTable mplsOutSegmentEntry
DC MPLS
LMGR OUT
LSR MPLS SEGMENT MPLS MPLS
ENTITY OUT TOP OUT OUT
LSR SEGMENT LABEL SEGMENT SEGMENT
INDEX INDEX PTR XCINDEX OWNER
--------------------------------------------
1 2 3 snmp
3. do show DC-RLDF-MIB dcLmgrLdfFtnTable dcLmgrLdfFtnEntry
DC DC DC DC DC DC
LMGR DC LMGR DC LMGR LMGR LMGR LMGR LMGR
LDF LMGR DC LMGR DC LMGR LDF DC LMGR LDF FTN LDF LDF LDF LDF
FTN LDF DC LMGR LDF FTN LDF FTN DC LMGR FTN LDF FTN NHOP DC LMGR DC LMGR FTN FTN FTN FTN
LSR FTN LDF FTN FEC PRE IP ADDR LDF FTN TOP OUT IF ADDR LDF FTN LDF FTN VLAN NUM OUT OUT
INDEX VRF ID FEC TYPE LEN TYPE FEC ADDR LBL IDX TYPE NHOP ADDR NHOP MAC ID LBL LBL1 LBL2
-------------------------------------------------------------------------------------------------------------------------------------------
1 1 hostAddr 32 ipv4 28:00:04:20 40 16 ipv4 14:00:02:20 --ERROR-- 0 1 0 0

4. ngctl list
Check for these VNB nodes:
tnnlXX, mux_XX, mplsnhlfe_XX, mplsether_XX, split_eth1, mux_eth1
5. route -n
40.0.4.32 0.0.0.0 255.255.255.255 UH 5 0 0 tnnlXX
6. ip link show
An entry for interafce tnnlXX
XX = XC handle (unsigned long)
Test Input – 2
Using Spirent , send IP packet with dip = 40.0.4.32 port 9/3 .
Expected Output
Labeled packet (label = 40) should be received at port 9/4.
(Traffic is received at DUT on interface eth0 , DIP lookup is done and packet is forwarded via tnnlXX interface which in turn uses eth1 interface to eject packet )
## 3.7 Delete Static Ingress LSP
This test case is written to test deletion of a Ingress LSP . Deletion is user intended and caused by direct MIB configuration.
Test Input
Test case 3.1 and 3.6 followed by:
no DC-RLDF-MIB dcLmgrLdfFtnStaticTable dcLmgrLdfFtnStaticEntry 1 1 ipv4 28:00:04:20 32
commit
top
MPLS-LSR-STD-MIB mplsXCTable mplsXCEntry 1 3 0 2
commit
top
Expected Output
1. do show DC-RLDF-MIB dcLmgrLdfFtnTable dcLmgrLdfFtnEntry
% No entries found.
2. do show MPLS-LSR-STD-MIB mplsXCTable mplsXCEntry
% No entries found.
3. route -n
No route for 40.0.4.32 should exist .
4. ngctl list
These nodes should not exist :
tnnlXX, mux_XX, mplsnhlfe_XX, mplsether_XX, split_eth1, mux_eth1
5. ip link show
No entry for tnnlXX.
Test Input – 2
Using Spirent , send IP packet with dip = 40.0.4.32 port 9/3 .
Expected Output
No packet should be received at port 9/4.
(Traffic is received at DUT on interface eth0 , DIP lookup is done , no route is found and packet is dropped . )
## 3.8 Tunnel in Tunnel at Ingress
This test case is intended to test cases where two tunnels commence together at Ingress . DUT acts as ingress router . A tunnel is programmed which uses another underlying tunnel as transport Path.
Data Flow : IP packet is sent from port 9/3 towards eth0 of DUT. Outer tunnel label is pushed followed by underlying tunnel labels . And packet is forwarded out via out interafce of underlying tunnel (eth1) and received at STC-2 (port 9/4)
Test Input
Test case in 3.1 followed by:
MPLS-LSR-STD-MIB mplsOutSegmentTable mplsOutSegmentEntry 1 2
mplsOutSegmentInterface 16
mplsOutSegmentPushTopLabel true mplsOutSegmentTopLabel 40
mplsOutSegmentNextHopAddrType ipv4 mplsOutSegmentNextHopAddr 14:00:02:20
commit
top
MPLS-LSR-STD-MIB mplsXCTable mplsXCEntry 1 3 0 2 mplsXCAutoStaticXC yes mplsXCAdminStatus up mplsXCLspId 00:00:00:03
commit
top
DC-RLDF-MIB dcLmgrLdfFtnStaticTable dcLmgrLdfFtnStaticEntry 1 1 ipv4 28:00:04:20 32 dcLmgrLdfFtnStatOutLbl 40 dcLmgrLdfFtnStatOutIfIdx 16
commit
top
MPLS-LSR-STD-MIB mplsOutSegmentTable mplsOutSegmentEntry 1 4
mplsOutSegmentInterface IDX
mplsOutSegmentPushTopLabel true mplsOutSegmentTopLabel 50
commit
top
MPLS-LSR-STD-MIB mplsXCTable mplsXCEntry 1 5 0 4 mplsXCAutoStaticXC yes mplsXCAdminStatus up mplsXCLspId 00:00:00:05
commit
top
DC-RLDF-MIB dcLmgrLdfFtnStaticTable dcLmgrLdfFtnStaticEntry 1 1 ipv4 38:00:04:20 32 dcLmgrLdfFtnStatOutLbl 50 dcLmgrLdfFtnStatOutIfIdx IDX
commit
top
--Here IDX is interafce index of tnnlXX created in linux .
--Get index using command ip link show
Expected Output
1. do show MPLS-LSR-STD-MIB mplsXCTable mplsXCEntry
DC
LMGR MPLS MPLS
LSR MPLS MPLS XCIN XCOUT
ENTITY XCIN XCOUT MPLS SEGMENT SEGMENT
LSR MPLS SEGMENT SEGMENT MPLS XCOPER IF IF
INDEX XCINDEX INDEX INDEX XCOWNER STATUS INDEX INDEX
----------------------------------------------------------------------
1 3 0 2 snmp up 0 16
1 5 0 4 snmp up 0 41
2. do show MPLS-LSR-STD-MIB mplsOutSegmentTable mplsOutSegmentEntry
DC MPLS
LMGR OUT
LSR MPLS SEGMENT MPLS MPLS
ENTITY OUT TOP OUT OUT
LSR SEGMENT LABEL SEGMENT SEGMENT
INDEX INDEX PTR XCINDEX OWNER
--------------------------------------------
1 2 3 snmp
1 4 5 snmp
3. do show DC-RLDF-MIB dcLmgrLdfFtnTable dcLmgrLdfFtnEntry
DC DC DC DC DC DC
LMGR DC LMGR DC LMGR LMGR LMGR LMGR LMGR
LDF LMGR DC LMGR DC LMGR LDF DC LMGR LDF FTN LDF LDF LDF LDF
FTN LDF DC LMGR LDF FTN LDF FTN DC LMGR FTN LDF FTN NHOP DC LMGR DC LMGR FTN FTN FTN FTN
LSR FTN LDF FTN FEC PRE IP ADDR LDF FTN TOP OUT IF ADDR LDF FTN LDF FTN VLAN NUM OUT OUT
INDEX VRF ID FEC TYPE LEN TYPE FEC ADDR LBL IDX TYPE NHOP ADDR NHOP MAC ID LBL LBL1 LBL2
-------------------------------------------------------------------------------------------------------------------------------------------
1 1 hostAddr 32 ipv4 28:00:04:20 40 16 ipv4 14:00:02:20 --ERROR-- 0 1 0 0
1 1 hostAddr 32 ipv4 38:00:04:20 50 41 unknown --ERROR-- 0 1 0 0
3. route -n
40.0.4.32 0.0.0.0 255.255.255.255 UH 5 0 0 tnnlXX
56.0.4.32 0.0.0.0 255.255.255.255 UH 5 0 0 tnnl1YY
4. ngctl list
Check for these vnb nodes:
tnnlYY, mux_YY, mplsnhlfe_YY, mplsnhlfe_YY_40, mplsether_YY,
tnnlXX, mux_XX, mplsnhlfe_XX, mplsether_YY,
split_eth1, mux_eth1
5. ip link show
two new interafces tnnlXX and tnnlYY
Test Input – 2
Using Spirent , send IP packet with dip = 56.0.4.32 port 9/3 .
Expected Output
Labeled packet (label = 40 | 50) should be received at port 9/4.
(Traffic is received at DUT on interface eth0 , DIP lookup is done and packet is forwarded via tnnlYY interface which in turn uses tnnlXX interface to forward packet )
## 3.9 Delete Tunnel in Tunnel at Ingress
This test case involves two deletion scenarios:
a) Outer tunnel is deleted
b) Underlying tunnel deleted
Test Input for a)
Test input for test 3.1 and 3.8 followed by :
no DC-RLDF-MIB dcLmgrLdfFtnStaticTable dcLmgrLdfFtnStaticEntry 1 1 ipv4 38:00:04:20 32
commit
top
no MPLS-LSR-STD-MIB mplsXCTable mplsXCEntry 1 5 0 4
no MPLS-LSR-STD-MIB mplsOutSegmentTable mplsOutSegmentEntry 1 4
commit
top
Expected Output
1. do show DC-RLDF-MIB dcLmgrLdfFtnStaticTable dcLmgrLdfFtnStaticEntry
        DC LMGR
DC LMGR DC LMGR LDF FTN DC LMGR DC LMGR
LDF FTN LDF FTN STAT FEC LDF FTN LDF FTN DC LMGR LDF
STAT STAT ADDR STAT FEC STAT FEC FTN STAT
LSR IDX VRF ID TYPE ADDR PRE LEN OPER STAT
-----------------------------------------------------------------
1 1 ipv4 28:00:04:20 32 operStatusUp

4. do show MPLS-LSR-STD-MIB mplsXCTable mplsXCEntry
DC
LMGR MPLS MPLS
LSR MPLS MPLS XCIN XCOUT
ENTITY XCIN XCOUT MPLS SEGMENT SEGMENT
LSR MPLS SEGMENT SEGMENT MPLS XCOPER IF IF
INDEX XCINDEX INDEX INDEX XCOWNER STATUS INDEX INDEX
----------------------------------------------------------------------
1 3 0 2 snmp up 0 16
2. route -n
No entry for route 56.0.4.32
3. ip link show
Only one tnnl interface exists tnnl_XX
4. ngctl list
These nodes will not exist :
tnnlYY, mux_YY, mplsnhlfe_YY, mplsnhlfe_YY_40, mplsether_YY
Test Input – 2 -A)
Using Spirent , send IP packet with dip = 56.0.4.32 port 9/3 .
Expected Output
No packet should be received at port 9/4.
(Traffic is received at DUT on interface eth0 , DIP lookup is done , no route exists and packet is dropped )
Test input for B)
Test case 3.1 and 3.8 followed by:
no DC-RLDF-MIB dcLmgrLdfFtnStaticTable dcLmgrLdfFtnStaticEntry 1 1 ipv4 28:00:04:20 32
commit
no MPLS-LSR-STD-MIB mplsXCTable mplsXCEntry 1 3 0 2
commit
Expected Output
1. do show MPLS-LSR-STD-MIB mplsXCTable mplsXCEntry
DC
LMGR MPLS MPLS
LSR MPLS MPLS XCIN XCOUT
ENTITY XCIN XCOUT SEGMENT SEGMENT
LSR MPLS SEGMENT SEGMENT MPLS MPLS XCOPER IF IF
INDEX XCINDEX INDEX INDEX XCOWNER STATUS INDEX INDEX
------------------------------------------------------------------------------
1 5 0 4 snmp lowerLayerDown 0 43
2.do show DC-RLDF-MIB dcLmgrLdfFtnStaticTable dcLmgrLdfFtnStaticEntry
        DC LMGR
DC LMGR DC LMGR LDF FTN DC LMGR DC LMGR
LDF FTN LDF FTN STAT FEC LDF FTN LDF FTN DC LMGR LDF
STAT STAT ADDR STAT FEC STAT FEC FTN STAT
LSR IDX VRF ID TYPE ADDR PRE LEN OPER STAT
-----------------------------------------------------------------
1 1 ipv4 38:00:04:20 32 operStatusUp
3. ngctl list
No such vnb node :
tnnlYY, mux_YY, mplsnhlfe_YY, mplsnhlfe_YY_40, mplsether_YY,
tnnlXX, mux_XX, mplsnhlfe_XX, mplsether_YY,
split_eth1, mux_eth1
4. route -n
No route entry for 40.0.4.32 and 56.0.4.32
5. ip link show
No interface entry for tnnlXX tnnlYY
Test Input – 2 -A)
Using Spirent , send IP packet with dip = 56.0.4.32 port 9/3 .
Expected Output
No packet should be received at port 9/4.
(Traffic is received at DUT on interface eth0 , DIP lookup is done , no route exists and packet is dropped )
## 3.10 Tunnel in Tunnel at Transit
This test case is intended to test cases where a Tunnel uses another tunnel as its transport path . DUT acts as transit router where underlying tunnel starts. A tunnel is programmed which uses another underlying tunnel as transport Path.
Data Flow : IP packet is sent from port 9/3 towards eth0 of DUT. Outer tunnel label is swapped followed by underlying tunnel label being pushed . And packet is forwarded out via out interafce of underlying tunnel (eth1) and received at STC-2 (port 9/4)
Test Input
Test case 3.1 followed by :
MPLS-LSR-STD-MIB mplsOutSegmentTable mplsOutSegmentEntry 1 2
mplsOutSegmentInterface 16
mplsOutSegmentPushTopLabel true mplsOutSegmentTopLabel 40
mplsOutSegmentNextHopAddrType ipv4 mplsOutSegmentNextHopAddr 14:00:02:20
commit
top
MPLS-LSR-STD-MIB mplsXCTable mplsXCEntry 1 3 0 2 mplsXCAutoStaticXC yes mplsXCAdminStatus up mplsXCLspId 00:00:00:03
commit
top
DC-RLDF-MIB dcLmgrLdfFtnStaticTable dcLmgrLdfFtnStaticEntry 1 1 ipv4 28:00:04:20 32 dcLmgrLdfFtnStatOutLbl 40 dcLmgrLdfFtnStatOutIfIdx 16
commit
top
MPLS-LSR-STD-MIB mplsOutSegmentTable mplsOutSegmentEntry 1 3
mplsOutSegmentInterface 98
mplsOutSegmentPushTopLabel true mplsOutSegmentTopLabel 50
commit
top
MPLS-LSR-STD-MIB mplsInSegmentTable mplsInSegmentEntry 1 3 mplsInSegmentInterface 15 mplsInSegmentLabel 35
commit
top
MPLS-LSR-STD-MIB mplsXCTable mplsXCEntry 1 4 3 3 mplsXCAutoStaticXC yes mplsXCAdminStatus up mplsXCLspId 00:00:00:04
commit
top
 Expected Output:
1. ngctl list
 Check for these nodes:
mplsnhlfe_YY, mplsnhlfe_YY_40, mplsether_YY,
tnnlXX, mux_XX, mplsnhlfe_XX, mplsether_YY,
split_eth1, mux_eth1, split_eth0, mux_eth0
2. do show DC-RLDF-MIB dcLmgrLdfFtnStaticTable dcLmgrLdfFtnStaticEntry
        DC LMGR
DC LMGR DC LMGR LDF FTN DC LMGR DC LMGR
LDF FTN LDF FTN STAT FEC LDF FTN LDF FTN DC LMGR LDF
STAT STAT ADDR STAT FEC STAT FEC FTN STAT
LSR IDX VRF ID TYPE ADDR PRE LEN OPER STAT
-----------------------------------------------------------------
1 1 ipv4 28:00:04:20 32 operStatusUp
3.do show MPLS-LSR-STD-MIB mplsXCTable mplsXCEntry
DC
LMGR MPLS MPLS
LSR MPLS MPLS XCIN XCOUT
ENTITY XCIN XCOUT SEGMENT SEGMENT
LSR MPLS SEGMENT SEGMENT MPLS MPLS XCOPER IF IF
INDEX XCINDEX INDEX INDEX XCOWNER STATUS INDEX INDEX
------------------------------------------------------------------------------
1 3 0 2 snmp up 0 16
1 4 3 3 snmp up 15 45
4. route -n
40.0.4.32 0.0.0.0 255.255.255.255 UH 5 0 0 tnnlXX
5. ip link show
interface by the name tnnlXX
XX= XC handle assigned by CP (unsigned long)
Test Input – 2 -A)
Using Spirent , send MPLS packet (label = 35) from Spirent port 9/3 .
Expected Output
MPLS packet (label = 40 | 50 ) should be received at Spirent port 9/4
(Traffic is received at DUT on interface eth0 , label is configured to perform a swap operation followed by exit via tnnl interafce )
## 3.11 Delete Tunnel in Tunnel at Transit
This test case involves two deletion scenarios:
a) Outer tunnel XC is deleted
b) Underlying tunnel deleted
Test Input for a)
Test input for test 3.1 and 3.10followed by :
no MPLS-LSR-STD-MIB mplsXCTable mplsXCEntry 1 4 3 3
commit
top
no MPLS-LSR-STD-MIB mplsInSegmentTable mplsInSegmentEntry 1 3
commit
top
no MPLS-LSR-STD-MIB mplsOutSegmentTable mplsOutSegmentEntry 1 3
commit
top
Expected Output
1. DC
LMGR MPLS MPLS
LSR MPLS MPLS XCIN XCOUT
ENTITY XCIN XCOUT SEGMENT SEGMENT
LSR MPLS SEGMENT SEGMENT MPLS MPLS XCOPER IF IF
INDEX XCINDEX INDEX INDEX XCOWNER STATUS INDEX INDEX
------------------------------------------------------------------------------
1 3 0 2 snmp up 0 16
2. ngctl list
These nodes no longer exist:
mplsnhlfe_YY, mplsnhlfe_YY_40, mplsether_YY, mux_eth0, split_eth0
Test Input for b)
Test case 3.1 and 3.10 followed by:
no DC-RLDF-MIB dcLmgrLdfFtnStaticTable dcLmgrLdfFtnStaticEntry 1 1 ipv4 28:00:04:20 32
commit
top
no MPLS-LSR-STD-MIB mplsXCTable mplsXCEntry 1 3 0 2
commit
top
Expected Output
1. do show MPLS-LSR-STD-MIB mplsXCTable mplsXCEntry
DC
LMGR MPLS MPLS
LSR MPLS MPLS XCIN XCOUT
ENTITY XCIN XCOUT SEGMENT SEGMENT
LSR MPLS SEGMENT SEGMENT MPLS MPLS XCOPER IF IF
INDEX XCINDEX INDEX INDEX XCOWNER STATUS INDEX INDEX
------------------------------------------------------------------------------
1 4 3 3 snmp lowerLayerDown 15 45
2. do show DC-RLDF-MIB dcLmgrLdfFtnStaticTable dcLmgrLdfFtnStaticEntry
% No entries found.
3. ngctl list
None of these nodes should exist :
mplsnhlfe_YY, mplsnhlfe_YY_40, mplsether_YY,
tnnlXX, mux_XX, mplsnhlfe_XX, mplsether_YY,
split_eth1, mux_eth1, split_eth0, mux_eth0
Test Input – 2 -A)
Using Spirent , send MPLS packet (label = 35) from Spirent port 9/3 .
Expected Output
No packet should be received at Spirent port 9/4
(Traffic is received at DUT on interface eth0 , no associated label configuration exists, packet is dropped)
## 3.12 Label stacking at Ingress
This test case tests case where multipla labels are pushed together at ingress .
Test input-1
MPLS-LSR-STD-MIB mplsOutSegmentTable mplsOutSegmentEntry 1 4
mplsOutSegmentInterface 43
mplsOutSegmentPushTopLabel true mplsOutSegmentTopLabel 50
commit
top
MPLS-LSR-STD-MIB mplsLabelStackTable mplsLabelStackEntry 1 1 1 mplsLabelStackLabel 20
commit
top
MPLS-LSR-STD-MIB mplsLabelStackTable mplsLabelStackEntry 1 1 2 mplsLabelStackLabel 30
commit
top
MPLS-LSR-STD-MIB mplsXCTable mplsXCEntry 1 3 0 2 mplsXCAutoStaticXC yes mplsXCAdminStatus up mplsXCLspId 00:00:00:03 mplsXCLabelStackIndex 1
commit
top
DC-RLDF-MIB dcLmgrLdfFtnStaticTable dcLmgrLdfFtnStaticEntry 1 1 ipv4 28:00:04:20 32 dcLmgrLdfFtnStatOutLbl 40 dcLmgrLdfFtnStatOutIfIdx 16
commit
top
Expected Output
1. do show MPLS-LSR-STD-MIB mplsLabelStackTable mplsLabelStackEntry
DC
LMGR MPLS MPLS
LSR MPLS LABEL LABEL
ENTITY LABEL STACK STACK
LSR STACK LABEL LABEL
INDEX INDEX INDEX PTR
-----------------------------
1 1 1
1 1 2
2. do show MPLS-LSR-STD-MIB mplsXCTable mplsXCEntry
DC
LMGR MPLS MPLS
LSR MPLS MPLS XCIN XCOUT
ENTITY XCIN XCOUT SEGMENT SEGMENT
LSR MPLS SEGMENT SEGMENT MPLS MPLS XCOPER IF IF
INDEX XCINDEX INDEX INDEX XCOWNER STATUS INDEX INDEX
------------------------------------------------------------------------------
1 3 0 2 snmp up 0 16
3. ngctl list
Check for these VNB nodes:
tnnlXX, mux_XX, mplsnhlfe_XX, mplsnhlfe_XX_20, mplsnhlfe_XX_40, mplsether_XX, split_eth1, mux_eth1
4. route -n
40.0.4.32 0.0.0.0 255.255.255.255 UH 5 0 0 tnnlXX
5. ip link show
A new interface named tnnlXX
Test Input-2
Using spirent send IP packet with dip = 40.0.4.32 from port 9/3
Expected Output
MPLS labeled packet ( 40 | 20 | 30 ) should be received at port 9/4